MCD4 DEMUX
Analysis and Proposition

---
What can be done different
MCD2	Possible options
Overlap 1/4	Overlap 1/2, 1/8 ?
No window	Bartlett, Hann, others?
Discard overlap	Add overlap ? Discard overlap but not window?
Filter by IDFT (IFFT with zeros)	Filter by FIR ?
Oversample 1.5 to 3	Oversample more or less?

---
DEMUX FILTERING
Filtering can be done with the IDFT, but requires many FFT freq bins.
5% roll off,
 very hard to filter out
 the adjacent channels
Filtering can also be done with an FIR, which relaxes the requirement on the FFT and provide better performance.
BIG FFT (but not big enough)
IFFT
IDFT
SMALL FFT
IFFT
IDFT
FIR

---
A very simple approach
- ADC sampling clock 880MHz (700MHz BW)
- No rate converter buffers
- Single clock everywhere (220MHz)
- Overlap 1/2, with 1/4 window but no adding.
- Superior adjacent channel rejection using FIR.
- Low hardware cost.