DEMUX and RATE CONVERTER
By: Jean-Serge Cardinal

---
Introduction
Introduction
- This presentation will present various architectures for the DEMUX and RC (Rate Converter) along with the performance that can be achieved.
- The complexity of the implementation inside an FPGA for the architectures will not be addressed here.
- The performance analysis comes from a special tool that can fully characterize the DEMUX/RC by sweeping a tone across the frequency of interest. It is not using a modulated signal nor noise sources.

---
DEMUX/RC Analysis tool
DEMUX/RC Analysis tool

---
Properties of the DEMUX/RC
Properties of the DEMUX/RC
WIN
IFFT
OL
RC
RRC
- The DEMUX/RC is a filter bank.
- Each filter is linear but time variant.
- Since it's time variant it cannot be analyse with an impulse since the impulse reponse will vary depending on where the pulse is located
- Therefore, the filters are characterized by sweeping a CW tone across the frequency of interest.
- Since it is linear, the overlap of all the tones and their errors gives the EVM performance that will be obtained if averaging the EVM of a modulated signal over an infinite time.
FFT
WIN
IFFT
OL
RC
RRC
WIN
IFFT
OL
RC
RRC

---
FFT
REC
IFFT
OLD
R-C
RRC
FFT
REC
IFFT
OLD
R-C
FIR
FFT
RRC
IFFT
OLD
FIR
R-C

---
Simulation options
Simulation options
- There are three types of RC, linear, Farrow as in MCD2, and FLAT. FLAT is a Farrow interpolator but compensated by the RRC filter.
- RRC filter size is about IFFTsize x 7
- There's a new Overlap and Discard mode using Hanning window.
- Adjacent channels have equal amplitude
- Simulation of 7 consecutive FFT frames